ACCESS INSTALLATION

SCRUBMASTER

- MOUNT AND INSTALL ACCESS HARDWARE ON DASHBOARD. (LOCATION ?)

- YOU CAN PLUG THE EQUIPMENT HARNESS INTO THE BACK OF THE ACCESS HARDWARE. (SHOULD BE SUPPLIED WITH ACCESS HARDWARE)

- ATTACH THE RED WIRE AT CB2 WITH THE BLACK/RED WIRE INSIDE ELECTRICAL BOX. (BATTERY PLUS)

- ATTACH THE BLACK WIRE TO THE GROUND STANDOFF INSIDE ELECTRICAL BOX. (BATTERY MINUS)

- CUT THE BLACK/RED WIRE FROM THE E-STOP SWITCH POSITION 2 TO KEY SWITCH POSITION 1. (BACKSIDE OF DASHBOARD) THIS MAY BE ACCOMPLISHED CUTTING THE INPUT BLACK/RED WIRE AT THE KEYSWITCH POSITION 1.

- SPLICE IN THE BROWN/WHITE WIRE TO THE E-STOP SIDE.

- SPLICE IN THE BROWN WIRE TO THE KEY SWITCH SIDE.

- ATTACH/SPLICE IN YELLOW WIRE TO THE SEAT SWITCH CONNECTION TO THE DRIVE MOTOR CONTROLLER SIDE (YELLOW/ORANGE WIRE). THIS CAN BE DONE AT THE SEAT SWITCH JUMPER PLUG INSIDE ELECTRICAL BOX.

- SPLICE IN THE GREY WIRE TO KEY SWITCH POSITION 2 OR TO YELLOW WIRE LOCATED AT THE BATTERY METER POSITION 1. (BACKSIDE OF DASHBOARD)

- ATTACH THE ORANGE/WHITE WIRE TO CB4 WITH THE RED WIRE INSIDE THE ELECTRICAL BOX. (WIRE GOING TO RECOVERY VACUUM MOTOR)

- ATTACH THE GREY/WHITE WIRE TO THE MAIN SCRUB SWITCH POSITION 4. (BACKSIDE OF DASHBOARD)

- REMAINING WIRES NOT USED AT THIS TIME.

THIS SHOULD COMPLETE THIS INSTALLATION.

PLEASE REFER TO LABELED SCHEMATIC FOR REFERENCE.